I STEEL GIRDER WITH TIMBER
Reinforce I STEEL GIRDER by using timber for buckling

---
PRESENT STATE
The web and the girder stiffener must be welded together
Large amount of steel need to make STEEL GIRDER, therefore CO2 emission is incresing
Cost is very high

---
GOOD POINT OF RESEARCH
The girder stiffener is made from steel, We can reduce welded points by using timber and STEEl GIRDAR resistant to buckling
We can reduce CO2 emission
Maybe we can construct bridge low cost

---
RESARCHING MODEL
12000mm
Use timber instead of girder stiffener

---
PROGRESS OF MY ANALYSIS
Now checking theoretical values about the web and flange of the Marumori bridge

---
WHAT TO DO NEXT
More buckling analysis for many models of I steel girder
Check overall buckling and local buckling point
Compare which models are suitable