A study on joint for glued- laminated timber using steel
Numano Taisei

---
Background
The use of wood in structural members is increasingly required from the perspectives of promoting carbon neutrality and preserving the landscape.
Among these, laminated timber beams with inserted steel plates to reinforce low-stiffness wood are expected to be a promising hybrid timber component in the future.
When connecting laminated wood members using joints, the stiffness of the connection may decrease if there are defects in the laminated wood at the joint area.
reduction in stiffness….
Therefore, this study focuses on how to design joints that maintain structural stiffness.

---
Research Description
　・Material used in this analysis
Materials	Young’s modulus(N/mm2)	Poisson’s ratio	Yield stress(N/mm2)
Laminated wood	7500	0.4	24
ss400	206000	0.3	245
adhesive	※750~7500	0.4	-
※We adjust the Young’s modulus of the adhesive as shown above, and run the analysis.
  If we assume the adhesive is perfectly bonded, its Young’s modulus is the same as the 　 Wood ー7500N/mm².
  From that value, we lower its Young’s modulus to simulate poor bonding of the adhesive.

---
Model used
Surface load
Cross section
9700mm
100mm 90mm
10000mm
420mm 410mm
Top view
Loading surface
200mm✕(100+90)mm=38000mm2
The wood and steel plate are bonded together using adhesive
9mm
adhesive

---
Analysis Method
Analysis software : Salome-Maca2021
Types of analysis : Elastoplastic analysis
What is elastoplastic analysis ?
Elastoplastic analysis is a method used to evaluate the strength and deformation of structures by considering both elastic and plastic behavior of materials.

---
Analysis Method
In this study, the load is applied in 10 steps as a surface load.
For example, if a load of 1000N is applied, it is divided into 10
steps of 100N each.
After the analysis is completed, we focus on a specific point at the center of the beam’s cross-section to examine the stress, strain, and displacement.

---
Research results
Stress-load
Adhesive Young’s modulus
 ①E=750N/mm2
 ②E=3750N/mm2
 ③E=7500N/mm2
After yielding, the decrease in stress was more pronounced for smaller values of Young’s modulus.

---
Research results
Displacement-load
Differences in post-yield deformation were observed for each value of Young’s modulus.

---
Research results
Stress-strain
Similar behavior was observed for all values of Young’s modulus.

---
Summary and discussion
While the displacement and stress responses to loading varied depending on Young’s modulus, the stress-strain relationship was
nearly the same regardless of Young’s modulus.
Beam deformation in the plastic region increases with lower adhesive
Young’s modulus.
The more rapid decrease in stress with smaller Young’s modulus is
considered to be caused by defects in the adhesive.
The stress-strain curves behaved similarly for all three cases, probably
because the model used was simple and joint-free.
■
■
■
■

---
Future work
My research is still at a preliminary stage and has not yet reached the point of designing and analyzing joints. Therefore, I would like to create beam models with joints and conduct studies comparing them with joint-free models.

---
Thank you for listening